### Advanced Processor Design in Verilog

#### Overview
The Advanced Processor module is a highly functional Verilog-based processor designed to showcase key features of modern CPU design. This module integrates advanced concepts such as branch prediction, instruction caching, pipeline hazard management, and debugging utilities, making it a versatile and efficient solution for computational tasks. The design is parameterized, allowing customization for specific use cases.

#### Features
1. Branch Prediction
  1. Implements a 2-bit branch history table (BHT) for branch prediction.
  2. Tracks mispredictions and adjusts the program counter (PC) accordingly.
2. Instruction Cache
  1. Direct-mapped cache with configurable size (CACHE_SIZE).
  2. Improves instruction fetch performance by reducing memory access latency.
3. Pipeline Hazard Management
  1. Basic hazard detection with forwarding and stall mechanisms.
  2. Ensures smooth execution in a pipelined environment.
4. Extended Instruction Set
  1. Supports arithmetic (ADD, SUB), branching (BEQ), and memory operations (LOAD, STORE).
  2. Designed to be extendable for additional operations.
5. Debugging and Profiling
  1. Built-in cycle counter to measure clock cycles.
  2. Branch misprediction counter to monitor execution accuracy.

#### Inputs and Outputs
Signal	Direction	Description
clk	Input	System clock signal.
rst	Input	System reset signal (active high).
inst_in	Input	Instruction fetched from memory.
data_in	Input	Data fetched from memory for LOAD.
data_out	Output	Data to be written to memory for STORE.
pc_out	Output	Current program counter value (for debug).

#### Parameters
Parameter	Default Value	Description
INIT_PC	32'h0000_0000	Initial value of the program counter.
CACHE_SIZE	16	Number of cache lines for instruction cache.

#### Module Description
1. Fetch Stage:
  1. Fetches instructions from memory or the cache.
  2. Updates the program counter (pc) by default with a +4 increment.
2. Decode & Execute Stage:
  1. Decodes the opcode and executes corresponding operations (arithmetic, branching, memory).
  2. Includes branch prediction logic to handle conditional branches efficiently.
3. Memory Stage:
  1. Handles LOAD and STORE operations by interacting with data_in and data_out.
4. Debugging Utilities:
  1. Outputs the program counter (pc_out) for real-time debugging.
  2. Tracks and reports performance metrics like clock cycles and mispredictions.

#### How to Use
1. Integrate the Module
  1. Add the advanced_processor module to your Verilog project.
  2. Connect the inst_in and data_in signals to your memory system.
2. Configure Parameters
  1. Adjust CACHE_SIZE and INIT_PC as needed to fit your application.
3. Simulate and Debug
  1. Use the pc_out and counters to monitor performance and debug the system.

#### Future Enhancements
- Support for more complex hazard management techniques.
- Multi-level cache hierarchy.
- Superscalar architecture with multiple pipelines.
- Floating-point arithmetic unit integration.

#### File Structure
- advanced_processor.v: The Verilog module implementing the processor.
- testbench.v: A testbench file to verify the processor's functionality.

#### License
This module is provided under the MIT License. Feel free to use, modify, and distribute the code with proper attribution.

Enjoy building with the Advanced Processor! 🚀